Introduction to the LED subsystem
Michael Welling (m_w)
mwelling@ieee.org

---
whoami
Michael Welling
Founder, QWERTY Embedded Design, LLC
PCB Design
Linux Board Support
Firmware
Community Efforts
Beagleboard.org GSoC Mentor
96Boards.org Community Mezzanine Initiative
E-ale.org Instructor
KiCAD Training

---
Overview
- What’s an LED?
- History of LEDs
- History of the LED subsystem
- LED class interface
- LED triggers
- LED devicetree binding
- LED driver API
- Userspace LEDs driver
- Labs

---
What’s an LED?
Light emitting diode or LED is a semiconductor device that emits light when current passes through it.
This is due to a phenomenon called electroluminescence which occurs when an electron combines with a hole emitting a photon at the P-N junction.
[Speaker Notes: III–V semiconductors Group III – Boron group Group V – Nitrogen group]

---
What’s an LED?
Rs = (Vsupply – Vf) / If
[Speaker Notes: LED will glow after the potential exceeds the forward voltage. This is how much the voltage drops across the diode. A current limiting resistor is needed to avoid burning out the LED. The Imax and Vf are typically listed in the datasheet. Adjust R to set the desired brightness.]

---
What’s an LED?
[Speaker Notes: Image public domain from wikipedia.]

---
LED History
- This effect was first observed in 1907 by H.J. Round while experimenting with cat whisker detectors on various crystalline substances.
- Similar observation were made by Oleg Losev in 1927 at point contacts of silicon carbide. Losev went on to study the phenomenon in great detail and published several articles on the topic.
- In 1961, James R. Biard pioneered work on the first GaAs based infrared LED. TI received a patent for this invention and this would provide the foundation for the earliest visible spectrum LED.
- In	1962, Nick Holonyak invented the first visible light red GaAsP LED while working at GE.
  His work led to the commercialization of LEDs.
- In the 1970s, blue and green LEDs were invented through use of GaN. Herb Maruska, Wally Rhines, and Jacques Pankove pioneered this work and their work was the basis of high brightness blue LEDs developed in the early 1990s. White LEDs followed shortly thereafter.
[Speaker Notes: GaAs = Gallium arsenide GaAsP = Gallium arsenide phosphide GaN = Gallium nitride Semiconductor doping introduces impurities to create N-P junction. N-type semiconductors are doped with electron donors. P-type semiconductors are doped with electron acceptors. Holonyak also invented the red laser diode. Biard also invented optoisolater.]

---
LED subsystem history
First introduced to the mainline kernel in 2006 by Richard Purdie extending the work of John Lenz.
https://lwn.net/Articles/169919/
Previous maintainers included Richard and Bryan Wu.
Currently co-maintained by Jacek Anaszewski and Pavel Machek.
[Speaker Notes: Found through commit history and mailing list.]

---
LED subsystem
LED SUBSYSTEM
M: Jacek Anaszewski <jacek.anaszewski@gmail.com>
M: Pavel Machek <pavel@ucw.cz>
R: Dan Murphy <dmurphy@ti.com>
L: linux-leds@vger.kernel.org
T: git git://git.kernel.org/pub/scm/linux/kernel/git/j.anaszewski/linux-leds.git
S: Maintained
F: Documentation/devicetree/bindings/leds/
F: drivers/leds/
F: include/linux/leds.h
[Speaker Notes: Grabbed from the MAINTAINERS file.]

---
LED subsystem
List: linux-leds
Info:
This is the mailing list for Linux LEDS development
Archives:
http://www.spinics.net/lists/linux-leds/
[Speaker Notes: http://vger.kernel.org/vger-lists.html#linux-leds]

---
LED class interface
LEDs can be controlled from the Linux userspace using the sysfs interface provided in /sys/class/leds.
Each registered LED will be given a folder named with the following convention:
"devicename:color:function"
The folder will contains follow attribute files to control the LED:
  brightness – LED brightness
  max_brightness – Maximum available brightness
  trigger – Trigger for blinking the LED
  pattern – Allows user to apply a blinking pattern to the LED.
Complex triggers will expose additional attributes related to the trigger.
[Speaker Notes: https://www.kernel.org/doc/Documentation/leds/leds-class.txt]

---
LED triggers
heartbeat – triggers an LED to blink like a heartbeat
timer	– periodically triggers LEDs on and off
cpu* – triggers an LED to blink on cpu activity
ide-disk – triggers an on IDE disk activity
usb-host – triggers an LED on USB activity
mmc* – triggers an LED on MMC activity

---
LED triggers (cont)
gpio – triggers on GPIO events
oneshot – trigger on arbitrary event and stay on for a specified period of time
rfkill* – trigger on wireless power on/off
kbd* – trigger on keyboard event

---
Devicetree binding (GPIO)
LEDs connected to GPIO lines
Required properties:
- compatible : should be "gpio-leds".
Each LED is represented as a sub-node of the gpio-leds device. Each
node's name represents the name of the corresponding LED.

---
Devicetree binding (GPIO)
LED sub-node properties:
- gpios : Should specify the LED's GPIO, see "gpios property" in
  Documentation/devicetree/bindings/gpio/gpio.txt. Active low LEDs should be
  indicated using flags in the GPIO specifier.
- label : (optional)
  see Documentation/devicetree/bindings/leds/common.txt
- linux,default-trigger : (optional)
  see Documentation/devicetree/bindings/leds/common.txt

---
Devicetree binding (GPIO)
LED sub-node properties (cont):
- default-state: (optional) The initial state of the LED.
  see Documentation/devicetree/bindings/leds/common.txt
- retain-state-suspended: (optional) The suspend state can be retained.Such
  as charge-led gpio.
- retain-state-shutdown: (optional) Retain the state of the LED on shutdown.
  Useful in BMC systems, for example when the BMC is rebooted while the host
  remains up.
- panic-indicator : (optional)
  see Documentation/devicetree/bindings/leds/common.txt

---
Devicetree binding (GPIO)
#include <dt-bindings/gpio/gpio.h>
leds {
        compatible = "gpio-leds";
        hdd {
        label = "Disk Activity";
        gpios = <&mcu_pio 0 GPIO_ACTIVE_LOW>;
        linux,default-trigger = "disk-activity";
        };
};

---
Devicetree binding (PWM)
LED connected to PWM
Required properties:
- compatible : should be "pwm-leds".
Each LED is represented as a sub-node of the pwm-leds device. Each
node's name represents the name of the corresponding LED.

---
Devicetree binding (PWM)
LED sub-node properties:
- pwms : PWM property to point to the PWM device (phandle)/port (id) and to
  specify the period time to be used: <&phandle id period_ns>;
- pwm-names : (optional) Name to be used by the PWM subsystem for the PWM device
  For the pwms and pwm-names property please refer to:
  Documentation/devicetree/bindings/pwm/pwm.txt
- max-brightness : Maximum brightness possible for the LED

---
Devicetree binding (PWM)
LED sub-node properties (cont):
- active-low : (optional) For PWMs where the LED is wired to supply
  rather than ground.
- label : (optional)
  see Documentation/devicetree/bindings/leds/common.txt
- linux,default-trigger : (optional)
  see Documentation/devicetree/bindings/leds/common.txt

---
Devicetree binding (PWM)
pwmleds {
        compatible = "pwm-leds";
        kpad {
        label = "omap4::keypad";
        pwms = <&twl_pwm 0 7812500>;
        max-brightness = <127>;
        };
};

---
LED driver API
A driver wanting to register a LED class device for use by other drivers / userspace needs to allocate and fill a led_classdev struct and then call led_classdev_register or devm_led_classdev_register.
If the non devm version is used the driver must call led_classdev_unregister from its remove function before free-ing the led_classdev struct.

---
LED driver API
led_set_brightness:
it is guaranteed not to sleep, passing LED_OFF stops blinking.
led_set_brightness_sync:
for use cases when immediate effect is desired - it can block the caller for the time required for accessing device registers and can sleep, passing LED_OFF stops hardware blinking, returns -EBUSY if software blink fallback is enabled.

---
LED driver API
led_get_brightness:
Get the current LED brightness level.
blink_set:
Hardware accelerated blinking set. delay_on and delay_off passed and matched as closely as possible.

---
Userspace LEDs driver
Userspace LEDs driver allows a user to instantiate driver by opening /dev/uleds and writing a uleds_user_dev struct.
This can be useful for testing triggers and can also be used to implement virtual LEDs.
https://elixir.bootlin.com/linux/latest/source/tools/leds/uledmon.c

---
LAB
- Investigate LED devicetree bindings and corresponding sysfs entries.
- Use GPIO trigger to turn on the RBG’s Green LED when L button is pressed and the red when R button is pressed.
- Write a program to write hexadecimal codes to the seven segment LEDs.
- Write a program that reads the ADC from the light sensor and changes the brightness of the RGB’s Blue LED.